VGA Distributor

ITEM NO.:  VD04A  1 Input 4 Output VGA Distributor with Stereo Audio

VD04A allows a computer to display VGA video on 4 monitors simultaneously. Built in with stereo audio which is is ideal for classrooms, tradeshows, or in-store displays where high quality video on several monitors is needed.

Features:

- Connects computers with VGA graphics to four VGA monitors.

- Supports stereo audio.

- Output 1 support DDC function.

- Support up to 450Mhz bandwidth.

- Supports high resolution up to 1920 x 1200@60Hz.

- Cascadable for multi outputs.

View of Connection and Installation:

Specification:

| ITEM | VD04A |
| --- | --- |
| VGA Connector Input/Output | 15-pin D-sub x 5 ( RGB Analog．0.7 Vp-p 75Ω ) |
| Synchronous Signal | H/V Separated ( TTL )．Horizontal 30-95 KHz．Vertical 50-180 Hz |
| Resolution | 1920 x 1200 @ 60Hz ( Max ) |
| Stereo Audio Input/Output | Stereo Phone Jack 3.5mm x 5 ( 3Vp-p Max．10KΩ ) |
| Power Supply | DC 5V 1000mA．Ø 2.5mm |
| Power Consumption | 250mA ( Max ) |
| Dimensions | 253 x 138.5 x 40 ( mm ) |
| Weight g | 325 g |