DVI with USB CAT5 Extender

ITEM NO.:  DE01U

The DVI with USB CAT5 Extender allows DVI video and USB signals be transmitted up to 45 meters via two CAT5 UTP cable.  Used in pairs, the Extender is used in home or commercial applications as a smart, fast and cost-effective, eliminates costly and bulky DVI, USB cable.

Applications for classroom projector systems, boardroom systems, collaborative PC systems C-training systems, and tradeshows PC demo systems and medical information systems.

DVI with USB 1.1 CAT5 Extender over two CAT5

- Include DE01UT transmitter, DE01UR receiver, used in pairs via two CAT5E/6 cable to send DVI and USB signal.

- Built in 3 port USB Hub & USB Audio.

- Support high resolution up to 1920 x 1200.

- Transmission distance up to 45 meters at 1920 x 1080.

Installation View:

Panel View:

DE01UT (Remote unit)

DE01UR  (Local unit)

Recommend Cable:

Video Link Cable use high quality Cat.5e / Cat.6 UTP cable.

Data Link Cable use high quality Cat5/5e UTP cable.

Transmission Distance:

The transmission distance will be affected from different DVI equipment and cable quality.

Using Cat.5e cable up to 45M.at 1920 x 1200 resolution.

RJ45 Pin Configuration: TIA/EIA 568B Wiring standard

Video Link

1. Orange-white		TMDS DATA2 +

2. Orange			    TMDS DATA2 -

3. Green-white		TMDS CLOCK +

4. Blue				    TMDS DATA1 +

5. Blue-white			TMDS DATA1 -

6. Green				TMDS CLOCK -

7. Brown-white		TMDS DATA0 +

8. Brown				TMDS DATA0 -

Data Link

1. Orange-white		USB+

2. Orange			    GND

3. Green-white		USB-

4. Blue				    GND

5. Blue-white			RESERVE

6. Green				GND

7. Brown-white		RESERVE

8. Brown				GND

Button, Switch Instruciton:

DE01UR Back Panel：

POWER SW		DE01UR Power on/off

LED Indication:

DE01UT RJ-45：

VIDEO LINK

GREEN		DVI Power on

YELLOW	Not Detect MONITOR HPD signal

DATA LINK

GREEN		PC USB Power on

DE01UR Front Panel：

PWR / LINK		Power , Link on/off

BLUE		PC Power on

RED		    PC Power off, unlink

OFF		    DE01UR Power off

DE01UR Back Panel：

VIDEO LINK

GREEN		DVI Power on signal

YELLOW	Net Detect DVI Video Signal

DATA LINK

GREEN		USB Status Normal

Caution:

- The wiring must be away from electro magnetic equipment, i.e. microwave, wireless, high voltage cable…etc., to avoid any interference.

- All wiring is “straight-through” twisted pair cable, not being used for other LAN or telephone equipment.

Specification:

| ITEM NO. | DE01U |
| --- | --- |
| Resolution | Up to 1920 x 1200 @60Hz |
| Link Cable Distance | 45 Meters |
| Power Supply | 5V DC 2A Regulated |
| Power Consumption | 2000mA (Max) |
| Temperature | Operation: 0 to 55 C, Storage: -20 TO 85 c, Humidity: up to 95% |
| DIMENSIONS W x H x D mm | DE01UT : 82.5 × 62.5 ×29.5 mm | DE01UR : 145 × 96 ×37 mm |
| Weight g | DE01UT : 150g | DE01UR : 330g |