AUDIO PICK-UP BOX

ITEM NO.:  AA001, AA002

AA001   In line Audio pick up box

- One add-on mini audio box for all cameras which need audio function.

- High sensitive microphone (-65dB) and DC12V power regulator built-in box.

AA002   Audio pick up box

- Add-on mini audio box for all cameras that require an audio function.

- High sensitivity microphone (-65dB) with 45cm power/audio cable.

- Easy to install and ideal for all security surveillance needs.

- DC12V power operation.

Installation View:

AA001

AA002

Remark:  Since Hi sensitivity microphone, AA001/AA002 audio pick up box must be put at 5 meters away from monitor to avoid any audio reverberation.

Specification:

| ITEM NO. | AA001 | AA002 |
| --- | --- | --- |
| AUDIO OUTPUT | Max 2 V p-p |
| POWER SUPPLY | 12 VDC (+ / - 0.5V) |
| POWER CONSUMPTION | 10 mA |
| DIMENSIONS W x H x D mm | 40x14.5x8 (Audio Box) | 50x14x14 (Audio Box) |
| Weight g | 100 | 35 |
| STORAGE TEMPERATURE | –30 to +60℃ |
| OPERATING TEMPERATURE | –10 to +45℃ |